## Slide 1: MICROARCHITECTURAL ATTACKS Vitaly Shmatikov
Credit for many slides: Stanford CS 155

## Slide 2: Isolation in Modern Systems
Process cannot read memory of another process
User-level code cannot read memory of the OS kernel
JavaScript cannot read memory of the Web browser outside its sandbox
Virtual machine cannot read memory of another virtual machine
Code outside an SGX enclave cannot read memory protected by SGX

## Slide 3: Performance in Modern CPUs
Clock speed maxed out
  Pentium 4 reached 3.8 GHz in 2004
  Memory latency is slow and not improving much
To gain performance, need to do more per cycle…
Reduce memory delays: caches
Work during delays: speculative execution
While waiting to determine the value of a condition, guess which branch to take, execute, throw out results if guess is wrong

## Slide 4: Memory Caches
Caches hold local (fast) copy of recently accessed 64-byte chunks of memory
MAIN MEMORY
Set | Addr | Cached Data ~64B
0 | F0016280 31C6F4C0 339DD740 614F8480 | B5 F5 80 21 E3 2C.. 9A DA 59 11 48 F2.. C7 D7 A0 86 67 18.. 17 4C 59 B8 58 A7..
1 | 71685100 132A4880 2A1C0700 C017E9C0 | 27 BD 5D 2E 84 29.. 30 B2 8F 27 05 9C.. 9E C3 DA EE B7 D9.. D1 76 16 54 51 5B..
2 | 311956C0 002D47C0 91507E80 55194040 | 0A 55 47 82 86 4E.. C4 15 4D 78 B5 C4.. 60 D0 2C DD 78 14.. DF 66 E9 D0 11 43..
3 | 9B27F8C0 8E771100 A001FB40 317178C0 | 84 A0 7F C7 4E BC.. 3B 0B 20 0C DB 58.. 29 D9 F5 6A 72 50.. 35 82 CB 91 78 8B..
4 | 6618E980 BA0CDB40 89E92C00 090F9C40 | 35 11 4A E0 2E F1.. B0 FC 5A 20 D0 7F.. 1C 50 A4 F8 EB 6F.. BB 71 ED 16 07 1F..
Addr: 2A1C0700
Data: 9E C3 DA EE B7 D3..
Addr: 132E1340
Address:
132E1340
Data: AC 99 17 8F 44 09..
Addr: 132E1340
Data: AC 99 17 8F 44 09..
Fast
Slow
Fast
hash(addr) to map to cache set
132E1340
Evict to make room
AC 99 17 8F 44 09..
MEMORY
CACHE
2A1C0700
Data:
AC 99 17 8F 44 ..
CPU
Sends address, Receives data
Reads change system state:
Read to newly-cached location is fast
Read to evicted location is slow
Big, slow
(e.g. 16GB SDRAM)

## Slide 5: Virtual Machine
Software abstraction
  Behaves like hardware
  Encapsulates all OS and application state
Virtualization layer
  Extra level of indirection
  Decouples hardware, OS
  Enforces isolation
  Multiplexes physical hardware across VMs

## Slide 6: Cache Contention
Attacker VM
Victim VM
Main
memory
CPU data cache
1) Read in a large array (fill CPU cache with attacker data)
2) Busy loop (allow victim to run)
3) Measure time to read large array (load measurement)
Locations in cache occupied by victim will take longer to load
Information about victim’s use of cache revealed to attacker
Same hardware cache used by victim and attacker

## Slide 7: Cross-VM Side Channel
Modular Exponentiation (x, e, N):
let en … e1 be the bits of e
y ← 1
for ei in {en …e1}
y ← Square(y) (S)
y ← Reduce(y, N) (R)
if ei = 1 then
y ← Multi(y, x) (M)
y ← Reduce(y, N) (R)
return y // y = xe mod N
If ei = 1, execute “SRMR”
If ei = 0, execute “SR”
Sequence of function calls
reveals secret key
Secret key
ElGamal encryption algorithm
Secret 4096-bit encryption key

## Slide 8: Prime + Probe
Attacker VM
Victim VM
Main
memory
CPU cache
Runs (S) operation
Attacker VM
(each row represents cache set)
…
Scheduling
order on
CPU core
Victim VM
Runs (M) operation
Attacker VM
…
Timings correlated to (distinct) cache usage patterns of S, M operations
Can spy frequently (every ~16 μs) by exploiting scheduling
Interrupt
Interrupt

## Slide 9: Attack Stages
Cross-VM Side Channel Probing
Cache Pattern Classification
Noise Reduction
Code-Path Reassembly
Vectors of cache measurements
Sequences of SVM-classified labels
Fragments of code path
Stage 1
Stage 2
Stage 3
Stage 4

## Slide 10: Prime + Probe Feasibility
Setup for in-lab experimentation:
  Intel Yorkfield processor (4 cores, 32KB L1 instruction cache)
  Xen + Linux + GnuPG + libgcrypt
Best result:
  300,000,000 prime-probe results (6 hours)
  Over 300 key fragments
  Brute force the secret key in ~9800 guesses
Not practical in deployment settings
State-of-the-art Prime+Probe attacks:
Sinan Inci et al. 2016 “Cache Attacks Enable Bulk Key Recovery on the Cloud”

## Slide 11: Flush + Reload
Attacker VM
Victim VM
Main
memory
S instr
L1 instruction cache
Attacker VM
Each row represents a cache set
Scheduling order on CPU core
M instr
Interrupt
Slow
Fast
Runs (S)
operation
flush
flush
flush
flush
Fast time on S instr means victim performed S op
Yarom and Faulkner (2013)
Yuval Yarom

## Slide 12: Flush + Reload
Attacker VM
Victim VM
Main
memory
S instr
L1 instruction cache
Attacker VM
Each row represents a cache set
M instr
Interrupt
Slow
Fast
Runs (S)
operation
Victim VM
Attacker VM
Interrupt
Runs (M)
operation
Scheduling order on CPU core
Fast time on M instr means victim performed M op

## Slide 13: Attacking Square-and-Multiply
Modular Exponentiation (x, e, N):
let en … e1 be the bits of e
y ← 1
for ei in {en …e1}
y ← Square(y) (S)
y ← Reduce(y, N) (R)
if ei = 1 then
y ← Multi(y, x) (M)
y ← Reduce(y, N) (R)
return y // y = xe mod N

## Slide 14: Speculative Execution
  if (uncached_value == 1) // load from memory
  a = compute(b)
Branch predictor guesses if() is true based on past history
CPU speculatively executes compute(b) while value is being loaded
Slow
Must wait to execute this code until if() is known
After value arrives from memory…
Guess correct: save speculative work, performance gain (!!)
Incorrect: discard speculative work, ho harm (??)

## Slide 15: Problem: Side Effects
Architectural Guarantee:
Register values eventually match the result of in-order execution
Is making, then discarding mistakes
the same as in-order execution?
The processor executed instructions that were not supposed to run !!
The problem: these instructions can have observable side-effects
Speculative execution:
CPU performs incorrect calculations, then deletes mistakes
Notes: Prior history: branch predictor.

## Slide 16: Spectre and Meltdown
Speculative execution bugs in Intel x86, ARM, IBM processors + cache-based side channels (Flush+Reload)
Consequences: break memory protection and isolation in kernels, JavaScript sandboxes, hypervisors, other VMs, trusted execution enclaves (SGX), etc.
Notes: Prior history: branch predictor.

## Slide 17: Conditional Branch Attack (Variant 1)
Suppose unsigned int x comes from an untrusted caller
Execution without speculation is safe:
  array2[array1[x]*4096] not evaluated unless x < array1_size
What about with speculative execution?
if (x < array1_size)
y = array2[array1[x]*4096];

## Slide 18: Conditional Branch Attack (Variant 1)
Before attack:
  Train branch predictor to expect if() is true (e.g. call with x < array1_size)
  Evict array1_size and array2[] from cache
if (x < array1_size)
y = array2[array1[x]*4096];
Memory & Cache Status
array1_size = 00000008
Memory at array1 base:
8 bytes of data (value doesn’t matter) Memory at array1 base+1000:
09 F1 98 CC 90...(something secret)
array2[ 0*4096]
array2[ 1*4096]
array2[ 2*4096]
array2[ 3*4096]
array2[ 4*4096]
array2[ 5*4096]
array2[ 6*4096]
array2[ 7*4096]
array2[ 8*4096]
array2[ 9*4096]
array2[10*4096]
array2[11*4096]
  
Contents don’t matter
Uncached
Cached
only care about cache status

## Slide 19: Conditional Branch Attack (Variant 1)
if (x < array1_size)
y = array2[array1[x]*4096];
Memory & Cache Status
array1_size = 00000008
Memory at array1 base:
8 bytes of data (value doesn’t matter) Memory at array1 base+1000:
09 F1 98 CC 90...(something secret)
array2[ 0*4096]
array2[ 1*4096]
array2[ 2*4096]
array2[ 3*4096]
array2[ 4*4096]
array2[ 5*4096]
array2[ 6*4096]
array2[ 7*4096]
array2[ 8*4096]
array2[ 9*4096]
array2[10*4096]
array2[11*4096]
Contents don’t matter
Uncached
Cached
  
only care about cache status
Attacker calls victim with x=1000
Speculative exec while waiting for array1_size:
    Predict that if() is true
    Read address (array1 base + x) (using out-of-bounds x=1000)
    Read returns secret byte = 09 (in cache ⇒ fast )

## Slide 20: Conditional Branch Attack (Variant 1)
if (x < array1_size)
y = array2[array1[x]*4096];
Memory & Cache Status
array1_size = 00000008
Memory at array1 base:
8 bytes of data (value doesn’t matter) Memory at array1 base+1000:
09 F1 98 CC 90...(something secret)
array2[ 0*4096]
array2[ 1*4096]
array2[ 2*4096]
array2[ 3*4096]
array2[ 4*4096]
array2[ 5*4096]
array2[ 6*4096]
array2[ 7*4096]
array2[ 8*4096]
array2[ 9*4096]
array2[10*4096]
array2[11*4096]
Contents don’t matter
Uncached
Cached
  
only care about cache status
Attacker calls victim with x=1000
…
  Request mem at (array2 base + 09*4096)
  Bring array2[09*4096] into the cache
  Realize if() is false, discard speculative work
  Finish operation and return to caller

## Slide 21: Conditional Branch Attack (Variant 1)
if (x < array1_size)
y = array2[array1[x]*4096];
Memory & Cache Status
array1_size = 00000008
Memory at array1 base:
8 bytes of data (value doesn’t matter) Memory at array1 base+1000:
09 F1 98 CC 90...(something secret)
array2[ 0*4096]
array2[ 1*4096]
array2[ 2*4096]
array2[ 3*4096]
array2[ 4*4096]
array2[ 5*4096]
array2[ 6*4096]
array2[ 7*4096]
array2[ 8*4096]
array2[ 9*4096]
array2[10*4096]
array2[11*4096]
Contents don’t matter
Uncached
Cached
  
only care about cache status
Attacker calls victim with x=1000
…
Measures read time for array2[i*4096] for all i
Read for i=09 is fast (because cached!), reveals the value of the secret byte
Repeat with many x (10KB/s)

## Slide 22: Violating JavaScript Sandbox
index will be in-bounds on training passes, and out-of-bounds on attack passes
JIT thinks this check ensures index < length, so it omits bounds check in next line. Separate code evicts length for attack passes
Do the out-of-bounds read on attack passes!
Keeps the JIT from adding unwanted bounds checks on the next line
Leak out-of-bounds read result into cache state!
Need to use the result so the operations aren’t optimized away
“|0” is a JS optimizer trick (makes result an integer)
if (index < simpleByteArray.length) {
index = simpleByteArray[index | 0];
index = (((index * TABLE1_STRIDE)|0) & (TABLE1_BYTES-1))|0;
localJunk ^= probeTable[index|0]|0;
}
4096 bytes = memory page size
Browsers run JavaScript from untrusted websites, JIT compiler inserts bounds checks on array accesses
Speculative execution runs through safety checks…
Evict length/probeTable from JavaScript (easy), then use timing to detect newly-cached location in probeTable

## Slide 23: Indirect Branches (Variant 2)
Indirect branches can go anywhere, e.g., jmp[rax]
  If destination is delayed, CPU guesses and proceeds speculatively
  Find an indirect jmp with attacker-controlled register(s), then cause mispredict to a useful ‘gadget’
  y = array2[array1[x]*4096];
Attack steps:
  Mistrain branch prediction so speculative execution will go to gadget
  Evict address [rax] from cache to cause speculative execution
  Execute victim so it runs gadget speculatively
  Detect change in cache state to infer memory contents

## Slide 24
https://therecord.media/first-fully-weaponized-spectre-exploit-discovered-online/
March 1, 2021
Can dump /etc/shadow password file

## Slide 25: Mitigating Spectre: Restore Cache State
Idea: fully restore cache state when speculation fails
Insecure! Speculative execution can have observable side effects beyond the cache state
if (x < array1_size) {
y = array1[x];
do_something_observable(y);
}
occupy a bus (detectable from another core),
or cause EM radiation

## Slide 26: Mitigating Spectre: Remove All Branches?
DOOM with no branches:
one frame every ~7 hours

## Slide 27: Mitigating Spectre: Stop Speculation
if (x < array1_size)
LFENCE // processor instruction
y = array2[ array1[x]*4096 ];
  Insert LFENCEs manually?
  Often millions of control flow paths
  Too confusing - speculation runs 188++ instructions, crosses modules
  Too risky – miss one and attacker can read entire process memory
  Put LFENCES everywhere?
  Abysmal performance - LFENCE is very slow
  Not in binary libraries, compiler-created code patterns
  Insert by smart compiler?
  Protect only known bad patterns = unsafe
  Microsoft Visual C/C++ /Qspectre unsafe for 13 of 15 tests
⇒ Protect all potentially exploitable patterns
✓
Idea: insert LFENCE on all vulnerable code paths
Efficient, no impact on benchmark software
Transfers blame from CPU to software: “should of put an LFENCE here!”

## Slide 28: Meltdown
1 raise_exception();
2 // the line below is never reached
3 access(probe_array[data * 4096]);
Intuition

## Slide 29: Meltdown: Core Spy Code
1 rcx = kernel address
2 rbx = probe array
3 retry:
4 mov al, byte [rcx]
5 shl rax, 0xc
6 jz retry
7 mov rbx, qword [rbx + rax]
Access privileged memory
Multiply by page size
Read from an attacker’s (unprivileged) array at (secret value) * 212
Retry reading privileged memory
Attacker times accessing [rbx + rax] for different values of rax
When finds one that loads fast, learns sensitive byte

## Slide 30: Meltdown Mitigation
KAISER/KPTI (kernel page table isolation):
remove kernel memory mapping in user-space processes
  Some performance impact
  Some kernel memory still needs to be mapped

## Slide 31: More Attacks
Foreshadow
Rogue inflight data load (RIDL) and Fallout
ZombieLoad
Store-to-leak forwarding
All enable reading unauthorized memory (client, cloud, SGX)
Mitigating incurs significant performance costs